## Slide 1: Communication Protocol

## Slide 2: Classification of communication
Depending on the mode of data transfer it is classified as
SERIAL COMMUNICATION
PARALLEL COMMUNICATION

## Slide 3: Serial v/s Parallel
Uses single data line for data transfer
Suitable for long distance communication.(50feet)
Cheaper but slower
requires parallel in serial out shift register at TX and serial in parallel out shift register at RX.
Uses 8 or more data lines for data
Suitable for small distance communication.(15feet)
Transfer faster and expensive
Costlier extra circuit is not required
Serial Communication
Parallel Communication

## Slide 4: Transmission Modes

## Slide 5: METHODS OF SERIAL COMMUNICATION
SYNCHRONOUS SERIAL COMMUNICATION
ASYNCHRONOUS SERIAL COMMUNICATION

## Slide 6: SYNCHRONOUS v/s ASYNCHRONOUS
SYNCHRONOUS
Communication takes place between a transmitter and a receiver operating on synchronized clocks.
Transfers block of data at a time
start, stop and control and error correction sequences around large continuous data blocks
faster
ASYNCHRONOUS
Communication is performed between two (or more) devices which operate on independent clocks
Transfers Single byte at time
start, stop and parity bits around individual words
slower

## Slide 7: UART

## Slide 8: Features
TM4C123GH6PM microcontroller has got eight UART ports.
In the TI Launchpad, the UART0 port is connected to the ICDI (In-Circuit Debug Interface).
Standard asynchronous communication bits for start, stop, and parity.
Fully programmable serial interface characteristics
  5, 6, 7, or 8 data bits
  1 or 2 stop bit generation

## Slide 9: UART Connection

## Slide 10: UART DATA FRAME

## Slide 11
Start
Set Clock frequency
Enable Port A and UART0 Module
Configure Port A pin0 as RX and PortA pin 1 as Tx
Configure Pins as UART pins
Select the Clock Source for UART module
Set baud rate
Pass the data
SysCtlClockSet(SYSCTL_SYSDIV_4 | SYSCTL_USE_PLL | SYSCTL_XTAL_16MHZ| SYSCTL_OSC_MAIN);
SysCtlPeripheralEnable(SYSCTL_PERIPH_GPIOA);
SysCtlPeripheralEnable(SYSCTL_PERIPH_UART0);
GPIOPinConfigure(GPIO_PA0_U0RX);
GPIOPinConfigure(GPIO_PA1_U0TX);
GPIOPinTypeUART(GPIO_PORTA_BASE, GPIO_PIN_0 | GPIO_PIN_1);
UARTClockSourceSet(UART0_BASE, UART_CLOCK_PIOSC);
UARTStdioConfig(0, 9600, 16000000);
UARTprintf("Hello from Tiva\n");

## Slide 12: Assignment
Configure UART to receive data from PC.
Input
From
Keyboard
Output to Monitor
Microcontroller receives
Data via USB

## Slide 13: 16x2 LCD Display

## Slide 14: LCD Display Pins

## Slide 15: LCD Commands:
* | Hex | Command to LCD Instruction Register |
* ------------------------------------------------------
* 0X0F LCD ON , Cursor ON
* 0x01 Clear Screen
* 0x02 Return Home
* 0x04 Shift Cursor to Left
* 0x05 Shift Display right
* 0x06 Shift Cursor to Right
* 0x07 Shift Display left
* 0x0E Display On Cursor Blinking
* 0X80 Force Cursor to Beginning of First line

## Slide 16: LCD Command Continue
* 0XC0 Force Cursor to Beginning of Second line
* 0X38 2 lines and 5×7 matrix
* 0X83 Cursor line 1 position 3
* 0x3C Activate second line
* 0X08 Display OFF, cursor OFF
* 0X0C Display ON, cursor OFF
* 0XC1 Jump to second line, position 1
* 0XC2 Jump to second line, position 2

## Slide 17: Pin Functions
RS=0 INSTRUCTION
1 DATA REGISTER SELECTION
RW=0 REGISTER WRITE
1 REGISTER READ
E=1 ENABLE
0 Disable

## Slide 18: 4 bit Initialization

## Slide 19: Continue….

## Slide 20: Writing the command to LCD

## Slide 21: Writing Character to LCD Display

## Slide 22: Writing String to LCD